## Slide 1
Features
Microcontroller: STM32F767ZIT6
Memory: High-speed embedded memories (Flash memory up to 2MB, SRAM up to 512KB), External FRAM FM25V10-GTR with 1Mb capacity.
Connectivity: Ethernet (RJ45), USB, Wi-Fi (ESP8266-12F), Cellular (SIM800L)
Interfaces: Multiple UART, I2C, SPI, CAN, and GPIOs
Power Supply: 3.3V operation with on-board voltage regulation
Peripherals: PWM, ADC, DAC, RTC
Voltage Conversion: Integrated circuits convert 0-10V input to 1.8-3.6V for ADC pins
Digital Signal Generation: Can generate digital signals based on input voltage levels from 0-10V.
Output Voltage PWM Generation: Generates PWM signals from the output voltage of pins, enabling control of various devices.
Clock: 32.768 kHz for RTC, main clock with multiple frequency options

## Slide 2
Specifications
CPU: ARM Cortex-M7 core with FPU, operating at up to 216 MHz
Analog: 12-bit ADC, 12-bit DAC
Timers: Up to 22 timers, including general-purpose, basic, and advanced-control timers
Communication: Ethernet MAC 10/100, USB OTG FS, USB OTG HS, 2x CAN, SDMMC
Operating Conditions: -40°C to +85°C temperature range
Packaging: LQFP144
Power Supply: 5V DC for relay circuits, ensuring compatibility with standard power source
PWM Outputs: 16 channels
Analog Inputs: 24 channels, 12-bit ADC

## Slide 3
Applications
Smart Mobility:
Integration with sensors and actuators for autonomous vehicle testing.
- The STM32 board interfaces with various sensors such as LiDAR, cameras, and ultrasonic sensors to collect data for autonomous navigation.
Data Acquisition:
High-speed data logging and transmission for real-time analysis.
- The board’s high-speed interfaces enable the collection of large volumes of sensor data, which are critical for performance analysis.
Connectivity:
Ensuring reliable Wi-Fi, cellular, and Ethernet communication for connected vehicle infrastructure.
- The board supports multiple communication protocols, ensuring that vehicles remain connected to the network under various conditions.